## Slide 1
【TRA-S, M, L (transit spectroscopy)】
The NIRCam HgCdTe detectors can be read out at 10 µsec per pixel .
The Si:As detectors can be read out at 1µsec per pix (=1Mpix per second per array; 1Hz, Wada et al. 2012)
At least two reads per pixel requested to sample up the ramp.
Area for spectra on the detector plate; 160 x 275 (TRA-S; HgCdTe), 320 x 555 (TRA-M; HgCdTe), 385 x 1590 (TRA-L; Si:As)
The shortest exposure time; 0.9 sec (TRA-S), 3.5sec (TRA-M), 1.3sec (TRA-L)
The shortest ramp duration for transit spectroscopic observations is set to 4 sec. (nominal 10 sec)
The maximum net data production rate by TRA-S, TRA-M, and TRA-L becomes
18 bit/pixel x 160 x 275 / 4sec = 0.18 Mbps (TRA-S) [max]  0.072 Mbps (TRA-S) [nominal]
18 bit/pix x 320 x 555 / 4sec =0.80Mbps (TRA-M) [max]  0.32 Mbps (TRA-M) [nominal]
18 bit/pix x 385 x 1590 / 4 sec =2.75Mbps (TRA-L) [max] 1.10 Mbps (TRA-L) [nominal]
Note: we collect the data sampled both before and after the reset. We plan to differentiate the signals between before and after the reset. (16bit/pix  18bit/pix)
【TRA WFS】
・32 x 32 pixels are read out at 20Hz (0.05s).
18 bit/pix x 32 x 32 x 20Hz = 0.37Mbps
If we have more smarts in the MISC electronics so that it calculates the centroids, the data rate drops to an estimated: 20 Hz x 16 bits per (x,y) pair centroid = 0.32 kbps
Summary of observing modes and the data rate
[1] MIR Transit Spectroscopy--- “Avg Data Rate”; 1.86 Mbps [1.49 Mbps (TRA) + 0.37 Mbps (WFS)], “Max Data Rate”; 4.10 Mbps [3.73 Mbps (TRA) + 0.37 Mbps (WFS)] Pointed observation (TRA-S[2kx2k HgCdTe; 160x275]; ON, TRA-M[2kx2k HgCdTe; 320x555]; ON, TRA-L[2kx2k Si:As; 385-1590]; ON, WFS[2kx2k HgCdTe; 32x32]; ON) TRA-S, TRA-M and TRA-L share the same FOV by means of beam splitter and are operated simultaneously. WFS will be operated in parallel to measure the drift.
Data rate for MISC observing modes (Baseline)